## Slide 1: X-ray tomography at GTK
What is the new device and what can it do?
XCT launch meet 9.11.2017

## Slide 2
X-ray tomography - principles
Sample is rotated and projections are recorded from all sides
Projections can be reconstructed into a 3D absorption coefficient map
Essentially a 3D density map
Non-destructive
© Samuli Siltanen

## Slide 3
Existing tomography devices in Finland
Stora Enso, JYU and UTU were first
Now devices at least in
  Helsinki
  Tampere
  Kuopio
  Oulu
6 Bruker Skyscan (1072, 1172, 1272)
3 Zeiss Xradia (microCT-400, nanoCT)
Several PET/CT devices

## Slide 4
How and why was the GTK device acquired?
2013 Sayab Muhammad joins GTK
  Idea about investigating rock morphology with XCT
  First sample scanned at Helsinki University
  Sayab, et al., High-resolution X-ray computed microtomography: A holistic approach to metamorphic fabric analyses. Geology 43 (1): 55-58 (2015)
2014 a talk about using XCT to decipher microstructures
  Interest within GTK
Academy application within the RAMI network
  2015 funding granted
  2017 device installed

## Slide 5
GE phoenix v|tome|x s 240
Manufactured in Wunstorf, Germany
240 kV / 320 W microfocus tube
  Most powerful in Finland!
180 kV / 15 W nanofocus tube
400×400 mm2 4 Mpix detector

## Slide 6
GE phoenix v|tome|x s 240
240 kV / 320 W microfocus tube
  Resolution up to 5 μm
  Allows imaging of complete drill core samples
180 kV / 15 W nanofocus tube
  Resolution up to 900 nm
400×400 mm2 4 Mpix detector
  Max. sample size 26×41 cm2 / 10 kg
  FOV width = 2000 pix
fast|scan module
  Along with high power enables short scan times when necessary (<30 min)

## Slide 7
Deben sample stage
Compression and tension
  Force up to 5 kN
  Displacement up to 10 mm
Cooling and heating
  Peltier elements at both ends of the sample
  Elements controlled independently
  -20 to 160 °C

## Slide 8
FEI PerGeos
Powerful tool for image processing
Noise filtering
Segmentation
  Watershed reduces operator-dependency
  Recipes increase efficiency
Analysis
  Grain orientation
  Pore size distribution
Visualization

## Slide 9
Sample sizes
Diameter 1,8 mm for best resolution
Max. Diameter 26 cm and height 41 cm
Everything in between!
1.8 mm
26 cm

## Slide 10
Applications
Grain orientations of gravel samples through the sample holder
Orientation analysis for high density inclusions
Lake sediment layer analysis through the sample holder
Non-destructive imaging of invaluable samples
Before – after analysis for rock fractures
3D shape inspection

## Slide 11
Case: Lieksa iron meteorite
First iron meteorite found in Finland
Max. thickness 6,6 cm, mostly Fe-Ni compound
220 kV / 48 W: Inner structure along with volumetric fractions of iron and silicate phases – unattainable by any other method

## Slide 12
Case: Suaspalo gravel orientations
Gravel samples inside a plastic tube
Traditionally orientation is determined by hand from at least 100 rocks
Tomographic investigation takes a few hours
  Orientation determined from thousands of rocks

## Slide 13
Case: Nurmijärvi lake sediment
Lake sediment samples in a plastic tube
Traditional analysis is manual and time consuming
Tomographic investigation can be done with a rate of 30 cm / h.

## Slide 14
What’s ahead?
More users – we want to expand the userbase as much as possible
More sample variety – main focus is on geological samples, but we want to explore the capabilities of the device
Method development, user development – Moving forward through advanced userbase, increased sample variety and networking (FinTomo)
Better tomography

## Slide 15: Thank you!